## Slide 1
DCAITI-Project: Implementation of a Traffic Light Service on an (Android) Smartphone
Oday Kabha oday.kabha@ipk.fraunhofer.de
Yiyang Song yiyang.song@campus.tu-berlin.de
Yuanheng Mu johanmu1994@mailbox.tu-berlin.de
Supervisor: Birgit Kwella
Notes: <number>

## Slide 2
Overview
DCAITI -Projekt
06.01.2021
1
  Review of First Presentation
  Current Implementations
  Milestone

## Slide 3
1.1 Review of First Presentation: Background & System Architecture
DCAITI -Projekt
06.01.2021
1
SPaT & MAP
RSU
via automotive WiFi
Background
System Architecture

## Slide 4
1.2 Review of First Presentation: Tasks
DCAITI -Projekt
06.01.2021
1
  Request, analysis and visualization of traffic lights information
  Decision of driving strategy:
    Determination of signal group
    Generation of strategies
  Simulation and evaluation

## Slide 5
2.1 Current Implementations: Works about Client
DCAITI -Projekt
06.01.2021
1
Server:
FOKUS Traffic Light Service (simulated RSU)
Data to request:
SPaT & Map in JSON format
Authorization:
with TUB-Account
Functions:
Verify authorization,
Save username and password,
Hidden/Show password

## Slide 6
2.2 Current Implementations: Works about Traffic Light Monitor
DCAITI -Projekt
06.01.2021
1
JSON Parser for SPaT
Parameters of interest:
IntersectionState.movementStates -> traffic lights
MovementState.movementEvents -> phases
MovementEvent.phaseState
TimeChange.likelyTime
Phase states:
DARK,
PROTECTED_MOVEMENT_ALLOED,
PROTECTED_CLEARANCE,
STOP_AND_REMAIN,
PRE_MOVEMENT
Likely time:
Timepoint, the end of this phase state in the current or next hour, with the unit of 0.1 sec

## Slide 7
2.2 Current Implementations: Works about Traffic Light Monitor
DCAITI -Projekt
06.01.2021
1
Stop
Pre
Move
Clear
Current Time
Likely Time of State Stop
Time Left
Dark
Move
Clear
Traffic light phase example 1:
Traffic light phase example 2 and current state to determinate:

## Slide 8
2.3 Current Implementations: Works about Determination
DCAITI -Projekt
06.01.2021
1
Algorithm 1
Linear Regression
Not suitable for real lane, which often in curve not straight line
Source: https://de.wikipedia.org/wiki/Lineare_Einfachregression

## Slide 9
2.3 Current Implementations: Works about Determination
DCAITI -Projekt
06.01.2021
1
Algorithm 2
Min Distance to Lane
Needs to add points in the curve of Lane to decrease deviation
After estimating min dist. => return laneID which contains the desired point.

## Slide 10
2.4 Current Implementations: Works about Map View
DCAITI -Projekt
06.01.2021
1
Google Maps Platform API
Polyline:
Marker:
Google Map API Key
SupportMapFragment
The My Location layer:

## Slide 11
2.5 Current Implementations: Works about Simulation
DCAITI -Projekt
06.01.2021
1
Routes Information in KML File
The Lane of Bicycle with ID 100 selected to test
Decide which lane to use for the simulation

## Slide 12
2.5 Current Implementations: Works about Simulation
DCAITI -Projekt
06.01.2021
1
Simulate route in Android Emulator

## Slide 13
2.5 Current Implementations: Works about Simulation
DCAITI -Projekt
06.01.2021
1
Route of pedestrian with Speed 3X: around 13.5km/h
Simulating Result

## Slide 14
3. Milestone
DCAITI -Projekt
06.01.2021
1

## Slide 15
Thanks for your attention!
Oday Kabha oday.kabha@ipk.fraunhofer.de
Yiyang Song yiyang.song@campus.tu-berlin.de
Yuanheng Mu johanmu1994@mailbox.tu-berlin.de
Notes: <number>