## Slide 1
DCAITI-Project: Implementation of a Traffic Light Service on an (Android) Smartphone
Oday Kabha oday.kabha@ipk.fraunhofer.de
Yiyang Song yiyang.song@campus.tu-berlin.de
Yuanheng Mu johanmu1994@mailbox.tu-berlin.de
Supervisor: Birgit Kwella
Notes: 1

## Slide 2
Overview
DCAITI -Projekt
06.01.2021
2
  Review of First Presentation
  Current Implementations
  Milestone

## Slide 3
1.1 Review of First Presentation: Background & System Architecture
DCAITI -Projekt
06.01.2021
3
SPaT & MAP
RSU
via automotive WiFi
  Background
  System Architecture

## Slide 4
1.2 Review of First Presentation: Tasks
DCAITI -Projekt
06.01.2021
4
Request, analysis and visualization of traffic lights information
Decision of driving strategy:
Simulation and evaluation
Determination of signal group
Generation of strategies

## Slide 5
2.1 Current Implementations: Works about Client
DCAITI -Projekt
06.01.2021
5
  Server:
  FOKUS Traffic Light Service (simulated RSU)
  Data to request:
  SPaT & Map in JSON format
  Authorization:
  with TUB-Account
  Functions:
  Verify authorization,
  Save username and password,
  Hidden/Show password

## Slide 6
2.2 Current Implementations: Works about Traffic Light Monitor
DCAITI -Projekt
06.01.2021
6
  JSON Parser for SPaT
  Parameters of interest:
  IntersectionState.movementStates -> traffic lights
  MovementState.movementEvents -> phases
  MovementEvent.phaseState
  TimeChange.likelyTime
  Phase states:
  DARK,
  PROTECTED_MOVEMENT_ALLOED,
  PROTECTED_CLEARANCE,
  STOP_AND_REMAIN,
  PRE_MOVEMENT
  Likely time:
  Timepoint, the end of this phase state in the current or next hour, with the unit of 0.1 sec

## Slide 7
2.2 Current Implementations: Works about Traffic Light Monitor
DCAITI -Projekt
06.01.2021
7
Stop
Pre
Move
Clear
Current Time
Likely Time of State Stop
Time Left
Dark
Move
Clear
  Traffic light phase example 1:
  Traffic light phase example 2 and current state to determinate:

## Slide 8
2.3 Current Implementations: Works about Determination
DCAITI -Projekt
06.01.2021
8
  Algorithm 1
  Linear Regression
  Not suitable for real lane, which often in curve not straight line
  Algorithm 2
  Min Distance to Lane
  Needs to add points in the curve of Lane to decrease deviation

## Slide 9
2.4 Current Implementations: Works about Map View
DCAITI -Projekt
06.01.2021
9
  Routes Information in KML File
  The Lane of Bicycle with ID 100 selected to test

## Slide 10
2.4 Current Implementations: Works about Map View
DCAITI -Projekt
06.01.2021
10
  Simulating route in Android emulator

## Slide 11
2.4 Current Implementations: Works about Map View
DCAITI -Projekt
06.01.2021
11
  Google Map API v2 Key for Map View
  com.google.android.gms.maps.SupportMapFragment

## Slide 12
2.4 Current Implementations: Works about Map View
DCAITI -Projekt
06.01.2021
12
  Simulating route in Android Emulator
  Route of pedestrian with Speed 3X: around 13.5km/h

## Slide 13
3. Milestone
DCAITI -Projekt
06.01.2021
13

## Slide 14
Thanks for your attention!
Oday Kabha oday.kabha@ipk.fraunhofer.de
Yiyang Song yiyang.song@campus.tu-berlin.de
Yuanheng Mu johanmu1994@mailbox.tu-berlin.de
Notes: 14