## Slide 1
DCAITI-Project: Implementation of a Traffic Light Service on an (Android) Smartphone
Oday Kabha oday.kabha@ipk.fraunhofer.de
Yiyang Song yiyang.song@campus.tu-berlin.de
Yuanheng Mu johanmu1994@mailbox.tu-berlin.de
Supervisor: Birgit Kwella
Notes: 1

## Slide 2
Overview
DCAITI -Projekt
10.02.2021
2
  Background
  Secure Android Application
  Features
  Layout
  General Class Diagram
  System Architecture
  Main Tasks (Implementation, Simulation and Test)
  Milestones
  Licenses

## Slide 3
GLOSA (Green Light Optimized Speed Advisory)
suggests speeds to vehicles to pass through an intersection
RSU (Roadside unit)
SPaT (Signal Phase and Time)
FOKUS Traffic Light Service
MAP (Map data)
Topology of the intersection
Road Users
car/ bicycle/ pedestrian
receive recommendation for action
1. Background
DCAITI -Projekt
3
SPaT & MAP
RSU
via automotive WiFi
Source: Lecture slides. First lecture
10.02.2021
Notes: 3

## Slide 4
2. Secure Android Application
DCAITI -Projekt
4
10.02.2021
Secure Java
Code
Secure XML
Code
Secure Class
Architecture
Application
Notes: 4

## Slide 5
3. Features
DCAITI -Projekt
5
10.02.2021
TrafficMonitor
Notification
Receiver
Location
Receiver
Shared
Preferences
Other Features
(see slide 8)

## Slide 6
4. Layout (Splash Screen)
10.02.2021
DCAITI -Projekt
6

## Slide 7
4. Layout (Main Screen)
10.02.2021
DCAITI -Projekt
7

## Slide 8
4. Layout (Popup Screen)
10.02.2021
DCAITI -Projekt
8

## Slide 9
4. Layout (Settings Screen)
10.02.2021
DCAITI -Projekt
9

## Slide 10
4. Layout (About Screen)
10.02.2021
DCAITI -Projekt
10

## Slide 11
5. General Class Diagram
10.02.2021
DCAITI -Projekt
11

## Slide 12
6. System Architecture
DCAITI -Projekt
10.02.2021
12
Login Activity
Main Activity
Splash Screen
Frontend
Location Receiver
Notification Receiver
Client Service
Backend
Local Resource
DCAITI Server
Android App
Lane Info
Map Info
Spat Info
User Info
JSON Data
Location Info

## Slide 13
7. Main Tasks
DCAITI -Projekt
10.02.2021
13
Request, analysis and visualization of traffic lights information
Determination of signal group
Generation of strategies

## Slide 14
7.1 Traffic Light Monitor: Implementation
DCAITI -Projekt
10.02.2021
14
Stop
Pre
Move
Clear
Current Time
Likely Time of State Stop
Time Left
Dark
Move
Clear
Traffic light phase examples:
Client
JSON Parser
State Calculator
Map View
Spat JSON
Traffic Light Objects
Current State & Time Left

## Slide 15
7.1 Traffic Light Monitor: Simulation & Test
DCAITI -Projekt
10.02.2021
15
  Traffic lights contain 11 signal groups in intersection 14052
  Every lane has one visual traffic light with the corresponding label about information of lane id and signal group id. Position Info from MapInfo JSON
  Test, validation with the live view of dcaiti website, almost synchronous but our traffic lights delay a little bit (less than one second)
Source: https://werkzeug.dcaiti.tu-berlin.de/0432l770/trafficlights/

## Slide 16
7.2 Determination: Implementation
DCAITI -Projekt
10.02.2021
16
Algorithm 1 :
Linear Regression -> Not suitable for real lane, which often in curve not straight line
Algorithm 2 :
Min. Distance to Lane Reference Points -> GPS not accurate at lane level
Algorithm 3 :
Driving mode & Min. Distance to Reference Points
Arm 1
Arm 2
Arm 3
Arm 4
Min. Distance to Reference Points
Driving mode
Which arm
Which lane at this arm
Determination Result

## Slide 17
7.2 Determination: Simulation & Test
DCAITI -Projekt
10.02.2021
17
  Testcases with handy at intersection 14052
    Simulation of the bicycle users with the corresponding four driving directions in right picture
    The determination results of lanes with id 100, 102, 104 and 106 are expected
Source : Photo of the arm 1 of intersection 14052 taken by Yiyang and contains bicycle lane 100

## Slide 18
7.2 Determination: Simulation & Test
DCAITI -Projekt
10.02.2021
18
  Test results with handy at intersection 14052
    The lanes with id 100, 102, 104 and 106 are determined successfully.

## Slide 19
7.3 Driving Strategies: Implementation
DCAITI -Projekt
10.02.2021
19
Vcurrent: current speed
Vmax: maximum permitted speed
Vmin: minimum permitted speed
Vc: calculated speed to reach the intersection in the remaining time
[1]
[2]
[3]
[6]
[5]
[4]
Stop
Pre
Move
Clear
[1]
[2]
[3]
[6]
[5]
[4]

## Slide 20
7.3 Driving Strategies: Simulation & Test
DCAITI -Projekt
20
  For example: the route of car with Speed 3X: around 45 km/h
  Route Simulation with Emulator
10.02.2021

## Slide 21
7.3 Driving Strategies: Simulation & Test
DCAITI -Projekt
10.02.2021
21
  Case No.1: Car;
  State: Move & Clear;
  Enough time to pass
  Case No.2: Car;
  State: Move & Clear;
  No enough time to pass, need to speed up
  Case No.3: Car;
  State: Move & Clear;
  No time to pass

## Slide 22
7.3 Driving Strategies: Simulation & Test
DCAITI -Projekt
10.02.2021
22
  Case No.4: Car;
  State: Stop & Pre;
  Very long time to wait for green (just stop)
  Case No.6: Car;
  State: Stop & Pre;
  Green light is about to come
  Case No.5: Car;
  State: Stop & Pre;
  Still a little time to wait for green (slow down)

## Slide 23
8. Milestones
DCAITI -Projekt
10.02.2021
23

## Slide 24
9. Licenses
DCAITI -Projekt
10.02.2021
24
Source of the traffic light image: http://silentsai.blogspot.com/
Google Map SDK for Android (API-Key apply):
https://console.cloud.google.com/google/maps-apis/

## Slide 25
Thanks for your attention!
Oday Kabha oday.kabha@ipk.fraunhofer.de
Yiyang Song yiyang.song@campus.tu-berlin.de
Yuanheng Mu johanmu1994@mailbox.tu-berlin.de
Notes: 25